## Slide 2: Fire Science
What elements are needed to start a fire?

## Slide 3: Common Fire Classifications
“Ordinary” combustibles
Paper, wood, rubber, plastics, and textiles.
“Flammable liquids”
Oil, gasoline, solvents
“Energized circuits”
Electrical equipment
and computers

## Slide 4: Class D Fires
Magnesium
Sodium
Potassium
Titanium
Zirconium
other flammable metals
D
COMBUSTIBLE
METALS

## Slide 5: Class K Fires
Fires involving combustible vegetable or animal non-saturated cooking fats in commercial cooking equipment.

## Slide 6: Common Extinguisher Features
Locking pin
Carrying handle / operating lever
Pressure gauge
Label :
  Type (Water, C02, Dry Chemical)
  Classification (A, B, C)
  NFPA capacity Rating
  Instructions
Discharge nozzle or horn

## Slide 7: Classification of Extinguishers
Letters indicate class of fire for which extinguisher can be used.
Numbers indicate effectiveness of the extinguisher when used by a non-expert.
D

## Slide 8: Common Types of Fire Extinguishers
Water
Dry Chemical
CO2
Halon
Dry Powder

## Slide 9: Water
Water + CO2 propellant
ONLY for Class fires
  wood / paper, etc.
Spreads burning liquids!
DANGER of electric shock if used on live circuits!

## Slide 10: DRY CHEMICAL Multi-Purposed Rated
Best for general use
Reduced risk of re-ignition
A 10 lb. unit empties in 8-10 secs.
  Effective range of 6 ft. to 15 ft.
Either
Or

## Slide 11: Carbon Dioxide C02
Best on burning liquids / electrical
SHORT range - 3 to 8 ft.
10- pound unit empties in 5 to 10 seconds!
  Use short spurts!
DISPERSES QUICKLY!
  Continue applying after the fire is out!
Unit gets VERY cold - hold properly

## Slide 12: Halon
Best for computers / electronics
Weight-for-weight TWICE as effective as C02
No residue, easy clean-up
VERY SHORT range, 3 to 6 ft.
Like C02, Discharges QUICKLY!
Like C02, Disperses QUICKLY!
  Continue after flames are extinguished

## Slide 13: Fire Extinguishers

## Slide 14: Inspection and Maintenance of Fire Extinguishers
NFPA requires extinguishers be inspected monthly, or more frequently if circumstances require it.
You must ensure that:
The extinguisher is not blocked by equipment, coats or other objects that could interfere with access in an emergency.
The pressure is at the recommended level. On extinguishers equipped with a gauge the needle should be in the green zone - not too high and not too low.
• The pin and tamper seal (if it has one) are intact.

## Slide 15: Fire Extinguisher Inspection
INSPECTION TAG:

## Slide 16: Extinguisher Maintenance
The NFPA says that maintenance should be performed at least Annually!
HOW OFTEN SHOULD MAINTENANCE BE PERFORMED?

## Slide 17: Fire Extinguishers
MAINTENANCE TAGS

## Slide 18: Use a portable extinguisher ONLY if the:
Building is being evacuated (Fire alarm has been pulled)
Fire Department has been called (Dial 911!)
Fire is NOT spreading (small and contained)
EXIT IS CLEAR (fight fire with your back to an exit )
Proper extinguisher is at hand, and...
  You have been trained and know how to use it!
  You use “Buddy System” - have someone back you up!
    Get assistance BEFORE trying to fight a fire!

## Slide 19: PASS
Sweep side to side
Aim low at the
base of flames
Squeeze the
handle
Pull the pin

## Slide 20: PULL the pin

## Slide 21: AIM
LOW at the base of the fire

## Slide 22: SQUEEZE
the lever

## Slide 23: SWEEP
from side to side

## Slide 24: OK, It’s out… Now What?
WATCH the fire area
  If the fire flares up again repeat!
  If you can’t control the fire, LEAVE immediately!
Call the fire department to inspect the scene!
Recharge or replace any used fire extinguisher!

## Slide 25
Questions?